## Slide 1: The CMS Particle Flow algorithm in CMS
Boris Mangano (ETH Zürich)
on behalf of the CMS collaboration

## Slide 2
Reconstruct & identify all stable particles in the event in a optimal way
Tracker
ECAL
HCAL
Magnet
Muon

## Slide 3
m
neutral hadron
charged hadrons
photon

## Slide 4
Particle Interaction & Detection
Detector measurements
From particles to PF particles
Analysis
as if it is done on generator level particles
“True” or generated particles
m
neutral hadron
charged hadrons
photon
Particle Flow reconstruction
PF particles
m
neutral hadron
charged hadrons
photon

## Slide 5
Particle flow past and present

## Slide 6
Particle flow and jets
Transverse view (x-y plane)

## Slide 7
Let’s consider for a moment a toy model for a calorimeter
Calorimeter response R is:
R=1 for E=20 GeV
R<1 for E<20 GeV
R>1 for E>20 GeV
Calorimeter resolution:
Can Tracker help Calorimeter also in this?
Calorimeter (Eecal + Ehad) resolution to hadrons:
For CMS,
stochastic term a ≈ 110-120%
Why is it so large and how can be reduced?

## Slide 8
50 GeV parton
“true” energy
20 GeV
10 GeV
20 GeV
fragmentation/hadronization
20 GeV
20 GeV
5 GeV
calorimeter
45 GeV
measured energy
50 GeV parton
30 GeV
20 GeV
35 GeV
20 GeV
55 GeV
40 GeV
Calorimeter resolution & response: fragmentation
50 GeV parton

## Slide 9
50 GeV parton
“true” energy
20 GeV
10 GeV
20 GeV
fragmentation/hadronization
20 GeV
20 GeV
5 GeV
calorimeter
45 GeV
measured energy
Measured jet energy depends on how the parton fragment
Calorimeter resolution & response: fragmentation

## Slide 10
20 GeV
21 GeV
20 GeV
19 GeV
Single particle energy measurement depends on intrinsic fluctuations of:
calorimeter sampling
showering
....
20 GeV hadron
20 GeV
calorimeter
single particle
20 GeV
20 GeV
Calorimeter resolution: intrinsic fluctuations

## Slide 11
20 GeV
10 GeV
20 GeV
reconstructed tracks
20 GeV
20 GeV
5 GeV
calorimeter clusters
Option 1:
subtract from calorimeter measurements the expected average energy deposit caused by the pointing tracks
reduces effect of parton fragmentation
measurement is still sensitive to intrinsic calorimeter resolution
“JetPlusTrack” or EnergyFlow approach
Tracker+Calorimeter: JetPlusTrack

## Slide 12
50 GeV parton
reconstructed particle
20 GeV
10 GeV
20 GeV
reconstructed tracks
20 GeV
20 GeV
5 GeV
calorimeter clusters
Option 2:
replace observed calorimeter cluster energy with the energy of the pointing/matched tracks
reduce effect of parton fragmentation
effectively replace calorimeter energy resolution with tracker momentum resolution for charged hadrons
neutral hadrons reconstruction still dominated by calorimeter resolution
Particle Flow approach
Tracker+Calorimeter: ParticleFlow

## Slide 13
Calorimeter jet:
  E = EHCAL + EECAL
  σ(E) ~ calo resolution to hadron energy: 120 % / √E
  direction biased (B = 3.8 T)
Particle flow jet:
  charged hadrons
    σ(pT)/pT ~ 1%
    direction measured at vertex
  photons/electrons
    σ(E)/E ~ 1% / √E
    good direction resolution
  neutral hadrons
    σ(E)/E ~ 120 % / √E
Still poor resolution, but neutral hadrons are the smallest component of the jet/event particles:
70% charged hadrons
20% photons
less than 10% neutral hadrons
A real case: CMS detector

## Slide 14
Jet energy resolution
Particle Flow converges to a calorimetric measurement at high pT when:
calorimetric clusters corresponding to different particles cannot be separated
calorimetric resolution is comparable or better than tracker one

## Slide 15
Calo Jets
PF Jets
PF jet response almost independent from the flavour of the jet-initiating parton
Jet energy response

## Slide 16
Particle flow is at its best in the reconstruction of taus: neutral hadron component (the component that is worst measured) is minimal
Tau reconstruction
Barrel
SIMULATION
particle flow
calorimeter-based
p0
p+
p+
p-
t

## Slide 17
MET resolution
Z pT > 100 GeV

## Slide 18
Electron reconstruction and Isolation

## Slide 19
The CMS Particle Flow:
  Improves the reconstruction of basically all physics objects (resolution improvement up to a factor 2X for Jets and MET)
  Makes analysis of data as if it is done on generator level particles
  Performs in data as expected from simulation
CONCLUSION
  Most analyses in CMS are now using Particle Flow

## Slide 20
The whole is greater than the sum of its parts (Aristotle)
Why particle flow ?

## Slide 21: Backup slides

## Slide 22: Backup slides on cluster-track linking

## Slide 23: Linking – ECAL view
Track impact within cluster boundaries  track & cluster linked

## Slide 24: Linking – HCAL view
Track impact within cluster boundaries  track & cluster linked
Clusters overlapping  clusters linked

## Slide 25: Links and blocks
Links:
  Track-ECAL
  Track-HCAL
  ECAL-HCAL
  Track-track
  ECAL-preshower
The block building rule:
  2 linked PF elements are put in the same blocks
ECAL
HCAL
Track
ECAL
Track
3 typical blocks

## Slide 26: Charged hadrons, overlapping neutrals
For each HCAL cluster, compare:
  Sum of track momenta p
  Calorimeter energy E
    Linked to the tracks
    Calibrated for hadrons
E and p compatible
  Charged hadrons
E > p + 120% √p
  Charged hadrons +
  Photon / neutral hadron
E<<p
  Need attention …
  Rare: muon, fake track

## Slide 27: Charged+neutrals: E ≈ p
Charged hadron energy from a fit of pi and E
  i = 1, .. , Ntracks
  Calorimeter and track resolution accounted for
Makes the best use of the tracker and calorimeters
  Tracker measurement at low pT
  Converges to calorimeter measurement at high E

## Slide 28: Charged+neutrals: E > p
Significant excess of energy in the calorimeters: E > p + 120% √E
Charged hadrons [ pi ]
Neutrals:
  E from ECAL or HCAL only:
    HCAL  h0 [ E – p ]
    ECAL  γ [ EECAL – p/b ]
  E from ECAL and HCAL:
    E-p > EECAL ?
      γ [ EECAL ]
      h0 with the rest
    Else:
      γ [ (E – p) / b ]
Always give precedence to photons

## Slide 29: Backup slides on tracker/tracking

## Slide 30
Huge silicon tracker
Hermetic
Highly efficient
TIB
TOB
Tracking system

## Slide 31
Huge silicon tracker
Hermetic
Highly efficient
But up to 1.8 X0
  Nuclear interactions
  g conversions
  e- brems
Tracking system

## Slide 32: Tracking
Efficient also for secondary tracks
Secondary tracks used in PF:
  Charged hadrons from nuclear interactions
    No double-counting of the primary track momentum
  Conversion electrons
    Converted brems from electrons
Nuclear interaction vertices
Displaced beam pipe!

## Slide 33: Backup slides on PF clustering

## Slide 34: PF Clustering
Used in:
  ECAL, HCAL, preshower
Iterative, energy sharing
  Gaussian shower profile with fixed σ
Seed thresholds
  ECAL : E > 0.23 GeV
  HCAL : E > 0.8 GeV

## Slide 35: PF Clustering
Used in:
  ECAL, HCAL, preshower
Iterative, energy sharing
  Gaussian shower profile with fixed σ
Seed thresholds
  ECAL : E > 0.23 GeV
  HCAL : E > 0.8 GeV

## Slide 36: Other Backup slides

## Slide 37
MET response

## Slide 38
Factor 2 improvement at low pT
Particle Flow converges to a calorimetric measurement at high pT when calorimetric clusters corresponding to different particles cannot be separated
Jet energy resolution (MC)

## Slide 39: Jets : η and ϕ Resolution
η
ϕ
1 HCAL tower

## Slide 40: Recipe for a good particle flow
Separate neutrals from charged hadrons
  Field integral (BxR)
  Calorimeter granularity
Efficient tracking
Minimize material before calorimeters
Clever algorithm to compensate for detector imperfections
PF Jet,
pT = 140 GeV/c
Data

## Slide 41
Strong magnetic field: 3.8 T
ECAL radius 1.29 m
BxR = 4.9 T.m
  ALEPH: 1.5x1.8 = 2.7 T.m
  ATLAS: 2.0x1.2 = 2.4 T.m
  CDF: 1.5x1.5 = 2.25 T.m
  DO: 2.0x0.8 = 1.6 T.m
PF Jet,
pT = 140 GeV/c
Data
Recipe for a good particle flow

## Slide 42: Neutral/charged separation (1) ECAL granularity
A typical jet
  pT = 50 GeV/c
Cell size:
  0.017x0.017
Good!

## Slide 43: Neutral/charged separation (2) HCAL granularity
A typical jet
  pT = 50 GeV/c
Cell size:
  0.085x0.085
  5 ECAL crystals
Bad…