## Slide 1
LHC Detectors:
Challenges
Achievements
Future
Nature at the Energy Frontier
Zürich, 3. June 2013
Roland Horisberger
Paul Scherrer Institute
Latsis Symposium 2013

## Slide 2
Find unknown toy particle X0
We will just produce in violent pp collision the new, unknown toy particle X0 here !
Particle X0 may be produced by:
Detector
Detector
my Little Hadron Collider
toy experiment
accelerated proton
accelerated proton
leaving remnant “proton”
leaving remnant “proton”
Detector  measure points of all pion trajectories
 calculate for all tracks
angles, momenta & charge
p + p  p+ + p- + X0 + p+ + p- + . . . . .
p+ + p-

## Slide 3
Measure for all particle: pi, mi, qi  4-vector
For many events try all 2 pion combinations and calculate their invariant mass mX by
Reconstructing the Puzzle
K.Stenson,B.Drell, K.Ulmer (Univ. Colorado)
CMS Experiment at LHC
Sunday, 6. Dec. 2009, 11:30
(from first 5h of colliding beam at 2x450GeV, run 123’596)
K0s  p+ + p-
Particle Data Group Value
K0 mass: 0.49765 GeV/c2
 correct combination of X0 will stick out statistically
from all incorrect combinations !
Principle of heavy particles reconstruction
Beauty-, Top- or SUSY and Higgs-Particles
is quite similar.
H  gg measure E1,2 & q1,2 of photons
Electromagnetic Calorimeter (ECAL)

## Slide 4
The Trouble with Experiments
Detector
Detector
Real detectors have:
finite mass  particle interactions (mult. scat., g-conversion, nucl. int.)
multiple event Pile-Up  track reconstruction: efficiency / fakes
finite resolution  merging detector hits
finite data rates  limited data samples, limit in statistics of rare physics
precise hits, 3D-pixel-points  separate hits, distinguish multiple PU vertices, sec. vtx
What can you do?
x
more layers  robustify track & event reconstruction
less mass  less particle interaction but in conflict to above
local data buffering, triggers & high speed links  heavy use of FE m-electronics
K0

## Slide 5
Proton collider experiments had gained valuable experience in detection and isolation of rare, high Q2-physics in large data volume of hadronic collisions. But other physics capabilities (e.g. beauty-physics) seemed marginal.
 high rate, messy environment, difficult event reconstruction, rad. damage
A young postdoc’s perception in late 80’s
 LHC detectors looked like very, very challenging project. (at least to me)
LEP experiments with new state of the art high tech detectors (e.g. silicon strips) under construction but not operated yet!
 low rate, clean simpler event reconstruction, no rad. damage
CERN study group for high energy colliders options:
- linear e+e- collider 1 TeV  machine very difficult, experiments easy
- pp colliders 16 TeV  machine “easy”, experiments challenging
Emerging LHC scenario (Aachen, 1990) with lower collision energy than SSC implied even more challenging detector parameters. Particle detection rate, DAQ data rates, radiation damage and background rejection capability were orders of magnitude beyond what ever had been done before.

## Slide 6
Timeline of Large Hadron Collider & Experiments
1980’s: Study groups compare e+e-, pp scenarios for machines, experiments & physics
1990 ECFA Aachen meeting: Physics, detector, machine,  CERN R&D projects
1992 Letter of Intend of experiments
1994 Technical Proposal of experiments
1996 - Technical Design Reports of Experiments (e.g. CMS Tracking Strips/Pixels 1998)
2000 Memorandum of Understanding
2000-04 Underground & experimental cavern work
2002-08 Construction of experiments
LHC start-up & incident / repair of damaged LHC sector 3-4
Experiments: calibrations, commissioning, cosmic muons data taking
LHC p-p-collisions & machine commissioning at 0.9 TeV & 2.76 TeV
2010 running at ~0.035 evts/fb at 7 TeV & Pb-Pb collisions
2011 running at ~ 5 evts/fb at 7 TeV & Pb-Pb collisions
2012 running at ~ 20 evts/fb at 8 TeV  Higgs boson discovered mH~125 GeV
2013 p-Pb collisions and start of a two years Long Shutdown LS1
 20 years from specific ideas to large experiments and physics success

## Slide 7
An Idea starts Everything
ECFA Aachen Workshop, 4. Oct 1990

## Slide 8
LHC Experiments
LHCb
weight 5’600 tons
height 10m
length 21m
~620 scientists
weight 10’000 tons
height 16m
length 25m
~1200 scientists
ALICE
CMS
weight 12’000 tons
height 18m
length 22m
~3000 scientists
weight 7’000 tons
height 22m
length 45m
~3000 scientists
ATLAS

## Slide 9
Detector performance of LHC experiments
Enormous growth (~105) of LHC luminosity since startup
Experiments constantly adapting
- algorithms
- FPGA firmware
- DAQ software
Problems showed up with rates !
Low lumi periods allowed debugging
Overall things have worked as planned !
 great success !
High channel segmentation of experiments has paid off (so far)
- operational channels (typ > 98% or better) & well calibrated
Flexibility in detector specific, low level digital data manipulation by FPGA’s has been crucial to this success story.  lesson for HL-LHC and other ambitions projects

## Slide 10
CMS
CMS ECAL
all sub-detectors in good shape
well calibrated & aligned
Trigger & DAQ runs ~100KHz
Data taking efficiency ~93%
jet energy resolution improved by particle-flow using tracker info
Silicon Strips ~200m2 !
alive channels : 98%
deconvolution mode (25ns)
Pixels pixel size = 100m x150m
- alive pixel channels : 97%
- Pixel threshold = 2500 e
- in-time threshold ~3200 e
- analog pulse height readout
measured position resolution:
rj = 12.7m +/- 2.3m
z = 28.2m +/- 1.9m
measured impact parameter (10GeV)
d (rj) = 25m
d (z) = 45m
analog pulse height readout

## Slide 11
CMS highlights
m-chambers with silicon/pixel tracker and 3.8T B-field allows excellent muon pT- resolution
primary vertex reconstruction of high pile up event
r-z-view of 78 vertices
Pixel Detector with excellent z-resolution and 2-track separation allow superbe reconstruction of multiple pp-interactions (pile up events)
residual [mm]
Residual Si-strip module
Tracker Alignment with Data (Milepede/HIP)

## Slide 12
Pulse
ATLAS
works very well
run efficiency 95.8% !
highly segmented Liquid Argon (LAr) calorimeter performs excellent in H gg
Pixels pixel size = 50m 400m
Pulse-height by ToT
Well adjusted pixel thresholds
alive pixel channels : 95% (80Mpixel, largest at LHC)
pixel threshold (in-time) = 3800e
meas. resolution: rj = 19m z =115m
Inner Tracker(|η|<2.5,B=2T):
Si pixels/strips, TRD
σ/pT~ 0.04%pT(GeV)⊕1.5%
ECAL(|η|<5):
Pb-LAr Accordeon
σ/E ~ 10%/√E ⊕0.7%
HCAL(|η|<5):
Fe/scintillator tiles (cen)
Cu/W-LAr (fwd)
σ/E ~ 50%/√E ⊕3%
Muon spectr. (|η|<2.7):
< 10% up to Eμ~ 1 TeV

## Slide 13
General Comment: remarkable agreement between Data & MC
Pb/scint. tile hadron calorimeter
Z e+e- electromagn. calorimeter
Performance muon spectrometer:
m reconstruction efficiency ~ 97%,
– constant for pT > 6GeV and |η|<2.7
– not affected by pile-up
mounting of muon chambers ~ mm
- after alignment position known ~40m

## Slide 14
LHCb
Luminosity leveling  L ~ 3∙1032 cm-2s-1
Experiment operates well (at 50ns) with μ ~ 1.5 beyond design of μ ~ 0.6
RICH works very well in complex events !
ATLAS/CMS
LHCb
Lumi Leveling by
displacing the beams
design
Remarkable little running inefficiency 1.4% due to VELO closing/opening to beam
VELO: Proper-time resolution
[LHCb-CONF-2012-02]
st = 45 fs
Bs–Bs oscillations measured
[LHCb-CONF-2011-50]

## Slide 15
LHCb: Particle Identification Performance
Plot with  hypothesis - No RICH
B0  K
B0  
Bs  KK
b p
b pK
[JHEP 10 (2012) 037]
from talk of Pascal Perret , LPC Clermont

## Slide 16
ALICE
Specialized on HI running but can do some things in pp
proves tracking at dN/dh ~6000
3 different silicon technologies
Silicon Drift Detector unique !
Calibration / Alignment of Silicon Drift Detectors
Impact parameter at 1GeV measured d (rj) ~ 60m !

## Slide 17
Did LHC Detectors meet our Expectations?
Answer is clearly YES:
all LHC experiments producing beautiful results
experiments mastered to readout 80-90M channel at unprecedented data rates
different sub-systems having failure rates of few % only
observed performance very close to expected (planned) performance
running at significantly higher #int/crossing than foreseen (50nsec LHC bx, LHCb)
experiments dealt with unexpected back-ground conditions (CMS pixel PKAM-events)
please remember, that any of the LHC Detectors is a unique prototype
BUT
construction, commissioning and running did not go without problems
each case individual and no simple recipe for preventing in future (upgrade)
relatively small number of dedicated physicists keep experiments running
commissioning and calibration is never over, the battle goes on!
Worry: who will re-start the experiments in 2015 after LS1? training? career path?

## Slide 18
Improvements and Upgrades
Data taking & physics analysis demonstrated eventual shortcomings of experiments
Upgrades due to:
  - previous staging decisions (limited resources)
  - different experimental conditions (LHC beyond design(>1034) , 50nsec operation)
  rather few due to poor decisions
Upgrades to experiments to be synchronized with LHC schedule
Upgrades divided into 3 Phases during Long Shutdowns (LS)
7/8TeV, Lint ~ 25 fb-1
LS1 2013-14 : Phase 0  ATLAS IBL (add 4th layer)
13/14 TeV, Lint ~ 100 fb-1
LS2 2018-19: Phase 1  CMS Pixel Upgrade (4 new layers) 2016/17
14TeV, Lint ~ 300 fb-1
LS3 2022-? : Phase 2  ATLAS & CMS replace complete tracker
14TeV, Lint ~ 3000 fb-1
A few proposed upgrades are presented: (appology to all others)
ATLAS Insertable B-Layer (IBL)
CMS Pixel Upgrade
LHCb & VELO Upgrades
Resistive MicroMega for ATLAS m-Chambers

## Slide 19
ATLAS IBL Upgrade
FE-I3 gets inefficient at HL-LHC
new FE-I4 ROC in 0.13m CMOS
new pixel size 50m x 250m
chip shows excellent behavior
- low pixel threshold ~1600 e
- very rad. tolerant
- low power (22mW/pixel)
trigger
storage
trigger
Trig’ed hits
buffering
data out 160Mb/s
in-pixel storage
trigger
18.8mm
200µm
long pixel 500µm
pixel 250µm
“standard“
Sensor options: planar n-in-n and 3D
Remarkable: planar sensor with ~200m pixel to edge
IBL installation in LS1 (2013-2014)

## Slide 20
CMS Pixel Upgrade
Pixel ROC modified for 2x1034
40MHz analog  160MHz digital
0.25m CMOS, 5Metals  6Metals
increase depth of
- data buffer 32  80
- timestamps 12  24
add readout buffer (64)
add 8 bit ADC for pulse height
1600 e in-time pixel thresholds
PKAM events  DAQ resync
mass production Q3 2013
Minimal changes to system
Vertexing in large PU events
 3 layers to 4 layers !!
Shift material to high h , CO2 cooling  reduced impact par. & g conversion
Modify ROC for 2x1034 operation
 reduce data loss at rL1=29.5mm
Pilot-system in LS1
Install few Pilot-Modules in existing FPIX for DAQ running in 2015/16
Operate DC-DC converters with present strip tracker.
new beam pipe
Supply Tube & UL Mechanics
DC-DC converters
Opto-Link at 400Mb/s
CO2 cooling
significant involvement by CH-consortium
Uni. ZH

## Slide 21
Performance in Vertexing & b-Tagging
(  50 PU)
Upgrade detector much more robust to pile up than current one.
Upgrade @ 50 PU ~ Current @ 0 PU  maintain physics capability or better at large PU
b-jet efficiency
~ 1.3x better
@ 10-2 udg-rej.
current
upgrade
Primary vertex res-olution improved by factor ~1.5 - 2
2 b-jets  (1.3)2 ~1.69
H  ZZ* 4 l
signal efficiency gain: H 4m +41%
H 2m2e +48%
H 4e +51%

## Slide 22
LHCb & Velo Upgrade
TORCH
RICH: change HPD’s to MAPMT’s
New Vertex
Detector
New Silicon Tracker
Calorimeters: replace R/O
5fb-1  50fb-1
open access allows simpler change
trigger limitations 1MHz  40MHz
software trigger with 20KHz output
should deal with int. rate m ~2.1
VELO Upgrade Options:
Strip detector: strip pitch 30m
VELOPIX , Timepix based 55mx55m
pixel ROC, large data rates output
PID Upgrade (keep RICH-1 & RICH-2)
HPD’s with 1MHz ROC  MAPMT’s 40MHz
Under development
@ Hamamatsu

## Slide 23
ATLAS m-Chamber Upgrade
Reduce forward muon fake rate
several technologies considered, show here:
Resistive MicroMegas
designed for tolerating sparks
resistive strip parallel to readout strip
Prototype (9cmx8cm) tested with neutrons ~106/cm2 . Shows no sparking compared to normal MM!
Technology is cheap  200m2
1.2m x 0.6m resistive MM

## Slide 24
Challenges to Tackle
HL-LHC Performance Estimates
( min. b* =15cm , CRAB cavities )
Parameter | nominal | 25ns | 50ns
N | 1.15E+11 | 2.0E+11 | 3.3E+11
nb | 2808 | 2808 | 1404
Peak Luminosity | 1 1034 | 7.4 1034 | 6.8 1034
Events/crossing | 19 | 141 | 257
worry ! (lumi leveling?)
Physics analysis with many overlapping PU events is likely to suffer from
  MET resolution
  jet energy resolution
  jet-jet separation
  Triggering problems  fast readout links are useful

## Slide 25
Missing Transverse Energy with CMS
In CMS different methods to calculate
Missing Transverse Energy (MET) :
Calorimeter MET
Track-corrected MET
Particle flow MET (pfMET)  best results
Missing Transverse Energy can be faked by
e.g. discharges or particle hits in photo-sensors !
Was dealt with careful algorithms !
MET degradation .vs. # PU events
How about 257 PU ?
 particle flow
F. Lacroix (U. Chicago / FNAL)

## Slide 26
High Granularity Particle Flow Calorimeters
M. Danilov, (ITEP), CALICE
Particle Flow Calorimeters have good chance to perform well even with many PU events.
Basic Particle Flow Algorithm:
Charged energy (65% in jet) – measure by tracking  separate multiple PU-events
Photon (25% in jet) – precisely measured in ECAL
neutrons / KL (only 10% in jet) – measured in HCAL with moderate resolution
Have to subtract away the charged energy in observed HCAL showers
Confusion error in separation of showers is dominant
Need a highly segmented HCAL detector 
calorimeter plane
90cm x 90cm
38 layers with 2cm Fe (W since 2011)
Scint. tiles with SiPM readout
CALICE AHCAL Prototype
depth segmentation is crucial
PF-Calos scaling like DE/E ~ 3%

## Slide 27
Insights, Technologies & “driving” Developments
Silicon sensors (basic material properties studies by RD50)
Irradiation in silicon sensors gives :
Surface damage from Ionizing Energy Loss (IEL)  surface charges (SiO2)
Crystal damage from Non-Ionizing Energy Loss (NIEL)  energy levels in bandgap
the latter leading to leakage current, trapping centers and doping effects.
Type Inversion (doping)
Normalize dose Feq to
damage of 1-MeV-neutrons

## Slide 28
leakage currents
charge trapping times
Observe the generation of universal, device doping independent
Signal charge trapping is dominant effect of irradiation at 1015neq and above !
charge collection distance

## Slide 29
Effective doping concentration Neff depends on radiation activated defects:
Epitaxial silicon diodes irradiated with:
23 GeV protons
reactor neutrons
Depending an radii, HL-LHC experiments will expose their silicon sensors more to charged hadrons or neutrons  pixels (more hadrons) & strips (more neutrons)

## Slide 30
Charge Collection in 3D Detectors
short charge collection distance
insensitive regions for tracks passing through electrode pillars. e.g. 900 tracks
interleaved electrode pillars  capacitance !
3D sensors show avalanche charge multiplication after irradiation. (seen also in planar)
 non gaussian sensor noise in read out
3D-silicon sensors planned in ATLAS ILB pixel upgrade

## Slide 31
Diamond Sensors
Particle detectors from Chemical Vapor Deposited (CVD) Diamond are trapping defect dominated.
Running construction projects:
- ATLAS Beam Conditions Monitor
- CMS Pixel Luminosity Telescope
- ATLAS Diamond Beam Monitor
Mono-crystalline diamonds show much better charge collection distances !
Mono- / Poly-crystalline Comparison
Poly-crystalline material shifted by ≈ 3.8 × 1015 p/cm2 to mono-crystalline material
(RD42, ETHZ)
Diamond pixel sensor can be operated at 3000K
Excellent thermal conductor  heat removal

## Slide 32
Role of micro-electronics is crucial
- reduce costs of highly segmented systems
- reduce power of digitisation/wave form sampling & read-out
- fast timing in highly segmented systems (very forward E/HCAL 20-30psec possibel )
- flexible detector specific digital data manipulations (FPGA)
Summary & Conclusions
LHC detectors have produced marvelous results and performed very well
Appologize for all the superbe sub-detector results not mentioned here
Remarkable physics performance of both GP LHC experiments, with rather different design choices
Each experiment is a unique prototype with its very unique problems
Not everything went perfect at all times, but ingenuity and dedication of people allowed to cope with problems, even beyond design boundary conditions
Commissioning & calibration continues  algorithmic performance upgrade
High speed data read-out links will play a crucial role in upgrade of LHC detectors

## Slide 33
HL-LHC with many Pile-Up events will challenge calorimeter based physics analysis
Tracker crucial in this task  particle flow  combined tracker-calorimeter design
Tracker needs to be designed for particle flow task  e.g. re-seeding at outer radii
However:
Feed back mechanism from physics to improved hardware not so clear established
Segregation of physics analysis community to detector builders is serious problem.
Hopes:
High eta region (2.5-4.5) detectors could be pioneered and could pionieer new very high performance technologies (pixels 1-2mm resolution , highly segmented calorimeter)  design cycle possibility for young LHC physicists.
Relatively low mass of the Higgs-like particle implies fairly soft pT spectrum
 must use relatively low threshold triggers under challenging pile-up conditions
 high speed data readout links (opto-links) could evtl. save us!

## Slide 34
Thank you for your attention !